SUB : Consolidated information on building projects completed during last three years.

Comprehensive information has been compiled in respect of building project completed in the recent past. Information at a Glance, furnished at page no. 7, shows that the cost of building varies from Rs. 400/- to 1039/- per Sq ft., depending upon several factors listed below:

- Safe soil bearing capacity :

SBC in the campus is 6 to 8 T/Sqm. Typically the SBC is 10 to 12 T/Sqm outside the campus. The soil investigation is conducted by Geo-Technical Department of IIT K. Low bearing capacity results in expensive foundation. Additional cost on this account is 2 to 3% of the total cost.

- Low lying site :

In depressed sites such as Hall-VII & VIII, the natural ground is filled to the extent of 90-cm. Retaining wall is also constructed below boundary wall in order to retain the earth. Development of site adds to the overall cost of the project.

- Boundary Wall :

The design of B/wall adopted in IITK is quite expensive in comparison to solid brick b/walls typically provided in Govt. Organizations, primarily due to the fact that the major portion is made of rugged iron grill.

- Landscaping :

Extensive landscaping work, comprising of ground profiling, access roads, toe walls / kerb stone on both sides of the roads, external lighting, fountains, underground sewage & drainage systems etc., is done in order to upgrade the surroundings and add grace to the building.

- External Services :

Water supply, sewer line, rainwater drain, power cable, chilled water grid line, telephone line and network line etc. have to be extended to the building under construction, from the existing service infrastructure. The element of cost is substantial.

- Two stage tendering :

For projects costing more than Rs. 2 (two) crores, we adopt a two stage tendering process in which only high-end contractors with proven track record are allowed to participate in the financial bid. This ensures high quality of work and by implication higher cost vis-à-vis run-of-the-mill Govt. Contractors.

- Higher Specifications  :

B&WC had taken a conscious decision to upgrade the specifications of work, while deliberating the specifications for CSE Building.  This had set the trend for all future works. The buildings constructed in IITK in the past three years are not comparable to conventional buildings constructed in the Govt. Departments. This adds substantially to the cost of project.

- Provision of high quality industrial products in the contract :

In order to control the quality of work, brands / make of high quality products are specified in the contract and thro’ various quality control procedures it is ensured that only specified products are used in the construction. This practice in IITK is contrary to Govt. Departments where no such provision is kept in the contract and it is possible, more often than not, to pass off substandard materials. While IIT system of contracting ensures good quality, it also adds to the cost.

- Testing of Materials :

All materials are tested in the IITK labs. in order to ensure reliable reports. On the contrary the Govt. departments get the materials tested in laboratories with doubtful integrity.

- Strict control on consumption of materials :

The materials brought by the contractor at site are first taken in stock by IWD supervisors and then issued to the contractor on day-to-day basis. Theoretical consumption is then compared with stocks and any short fall is recovered from his bills. Needless to mention that any material brought at site cannot be taken out of the campus without the approval of SE. This procedure completely discounts the possibility of pilferage of materials.

- Issue of cement & steel by the client :

The cost of cement & steel in a project constitutes 40% of the cost of civil work. If the contractor is required to purchase these materials, a large portion of his working capital is blocked. However if the client supplies the materials, the contractor is able to execute the project with a substantially lesser capital. Since IITK does not supply these materials, as per the guidelines of B&WC, cost of civil work goes up in comparison to the Govt. Projects where the client supplies cement & steel by investing its own capital.

- Project wise reports are enclosed in which the special features, having cost implication, are briefly mentioned.

- From the procedure for implementation of new projects, explained on page no. 4, it is evident that the cost of project is fully controlled by the administration, consultant, B&WC etc. thro’ various committees. The role of IWD essentially commences only after the award of work.

(Santosh Kumar)

Superintending Engineer

PROCEDURE FOR IMPLEMENTATION OF NEW PROJECTS FROM CONCEPT TO COMMISSIONING

| 1. | Space & facility requirement | Identified by user Group |
| --- | --- | --- |
| 2. | Location | Decided by SPAC Committee |
| 3. | Concept Plans | Prepared by Consultants Approved by User Group |
| 4.. | Detailed Specifications | Proposed by Architect as per Users requirement Approved by B & WC. |
| 6. | Estimates | Prepared by Consultant on the basis of Govt. Schedule of Rates Scrutinized by IWD Approved by B& WC. |
| 7. | Detailed working drawings ( Architectural & Structural) | Prepared by Consultant Approved by user group / Monitoring Committee IWD. |
| 8. | Processing of Preliminary Estimate | Prepared by consultant Scrutinized by IWD. Recommended by B&WC. Approved by BOG. |
| 9. | Processing of Detailed Estimate | Prepared by Consultant Scrutinized by EE, IWD Approved by SE, IWD. |
| 10. | Call of Tender i)Pre-qualification ii) Financial bid | Invited by IWD thro’ All India Publicity. Short listed by a committee, chaired by a senior Faculty appointed by Director. Short listed vendors approved by the Director. Invited and processed by IWD Accepted and approved by B & WC |
| 11. | Progress of Work | Monitored by IWD on day to day basis. Inspected by Monitoring Committee, from time to time. |
| 12. | Quality Control | Brands of the Industrial Products are specified in contract. No other material is allowed to be used. Samples of each material are approved by Architect & SE jointly and supplies checked by EE / AE before incorporation. All materials are tested in IITK laboratories as per CPWD /BIS codes and specifications. Field tests are conducted in site laboratory on day-to-day basis. Materials not qualifying the test are rejected and removed from site. No item is billed unless it is inspected by EE/AE and certified to be as per contract. Quantity of materials brought at site are compared with theoretical consumption and shortfall, if any is recovered. Only high end Contractors, with proven track record and qualifying the stringent eligibility criteria, are engaged thro’ the process of “Pre-Qualification.” Cement, Steel, bricks, tiles, paints, hardware, doors & windows, sanitary material, electrical cables/wires & fitting are directly sourced by the contractor from the specified manufactures to ensure originality. Purchases are verified from vouchers. Often the company officials are invited to check and certify the material brought at site. Cement & Steel are kept in the custody of IWD and issued to the Contractor on day-to-day basis. Only high quality materials are specified in the contract e.g. Steel is purchased from TISCO / SAIL etc. No material brought at site is allowed to be taken out the campus without a valid pass issued by SE and Security Officer. |
| 13. | Agencies controlling the quality and cost of work | B&WC Monitoring committee Test checking by EE / AE Superintending Engineer Chief Technical Examiners from CVC Internal Audit UP-AG audit |
| 14. | Agencies Controlling Labour welfare identification | EE, IWD Labour Commissioner (Central) |
| 15. | Rectification of defects, if any | Final inspection by SE before issuing mandatory completion certificate. Final inspection by Architect Final inspection by EE before initiating final measurements. Preparation of room wise report by AE and issuance of Test certificate. |
|  | Defect liability period | 6 months from the date of completion. |

_____________

| DETAILED INFORMATION ON PROJECTS AT A AGLANCE |
| --- |
| Sl. No. | Name of work | Year of construction | Plinth Area (Sqm) | A/A&E/S (in Lacs) | Actual Expenditure | Cost/Sqm (Rs.) | Cost/Sqft. (Rs.) |
|  |  |  |  |  | Civil | Elect. | A/C | Total |  |  |
| 1 | One additional block in Hall-IV (54 single seats) | 2000-2001 | 1210 | 79 | 44.55 | 7.55 | ---- | 52.10 | 4306 | 400 |
| 2 | One additional block in Hall-I (57 seats) | 1999-2000 | 1293 | 73 | 53 | 4 | ----- | 57 | 4386 | 408 |
| 3 | 2 nos. addl. blocks in Girls Hostel (120 seats) | 2002-2003 | 2054 | 130 | 100 | 16 | ---- | 116 | 5648 | 525 |
| 4 | One addl. block in Hall-V (54 seats) | 2002-2003 | 1095 | 49 | 54 | 10 | ---- | 64 | 5845 | 543 |
| 5 | RA Hostel | 2002-2003 | 2750 | 176 | 138 | 28 |  | 166 | 6036 | 561 |
| 6 | Hall of Residence for Boys No. VII (458 seats). | 2002-2003 | 12450 | 876 | 665 | 110 | ---- | 775 | 6225 | 579 |
| 7 | Hall of Residence for Boys No. VIII (459 seats). | 2003-2004 | 12850 | 875 | 700 | 105 |  | 805 | 6265 | 582 |
| 8 | Girls Hostel (250 seats). | 2000-2001 | 6159 | 412 | 340 | 52 | ---- | 392 | 6372 | 592 |
| 9 | 8 nos. Type-A & 4 nos. Type-B residences for Visiting Faculty. | 2002-2003 | 1380 | 101 | 83 | 11 | ---- | 94 | 6812 | 633 |
| 10 | SIDBI Innovation & Incubation Centre. | 2002-2003 | 1153 | 90 | 71 | 9 | ---- | 80 | 6964 | 647 |
| 11 | Biological Sciences & Bio Engineering Department. | 2002-2003 | 5800 | 481 | 337 | 79 | 45 | 461 | 7758 | 721 |
| 12 | Lecture Hall Complex (Phase.-I). | 2001-2002 | 2177 | 287 | 156 | 28 | 29 | 213 | 9784 | 909 |
| 13 | Computer Science & Engg. Department Building. | 2000-2001 | 3200 | 355 | 214 | 46 | 77 | 337 | 10531 | 979 |
| 14 | Samtel R&D Building. | 2002-2003 | 1547 | 195 | 112 | 30 | 31 | 173 | 11183 | 1039 |

LIST OF APPROVED MAKES  / MANUFACTURERS

The following industrial products are used in construction of buildings in IITK. These are some of the best products / brands available in the Indian Market  :

| Sl. No. | Details of Materials | Brand Name | Manufacturer’s Name |
| --- | --- | --- | --- |
|  | Paints & Primer: |  | Shall be first quality manufactures by : |
| 1. | Synthetic Enamel Paint | Apcolite Synthetic. Luxol Synthetic. iii) Nerolac Synthetic | i) Asian ii) Berger iii) Nerolac |
| 2. | Acrylic Washable Distemper | Tractor. Bison Nerolac Acrylic | i) Asian ii) Berger iii) Nerolac |
| 3. | Plastic Emulsion Paint | Royale Luxury Luxol Silk All Escape | i) Asian ii) Berger iii) Nerolac |
| 6. | White Cement | ---- | J.K. White ii) Birla White |
|  | Plywood Products : |  |  |
| 7. | Laminates | Sunmica / Formica Neoluxe iii) National | i) Bombay Burmah ii) Neoluxe India iii) National |
| 8. | Flush Door Shutters | Swastik (ISI) ii) Tower (ISI) | i) Kitply ii) Vidarbha Vineer |
| 9. | Pre Laminated Particle Board | Novopan | Novopan |
| 10. | Ply Wood, Block Board | Kitply Duroboard National Century | Kitply Sharada Ply National iv) Century |
| 11. | Ceramic Tiles ( 200 x 300mm ) | First Quality | i) Johnson ii) Kajaria iii) Somani |
| 12. | Glazed Tiles (100 x 200 mm) | First Quality. | Johnson Kajaria iii) Somani |
| 13. | Floor Dividing Strips | Fixopan PVC strips or equivalent | Fixopan Engineers |
| 14. | Mirror Glass, Window Panes |  | Asahi Float ii) Modi Float |
| 15. | Aluminum Section |  | Indal ii) Hindalco |
| 16. | M.S. Pipe |  | Prakash Jindal iii) QST |
| 17. | G.I. Pipes |  | Tata |
| 18. | Vitreous China Sanitary ware |  | Parryware Hindusta Sanitaryware iii) Cera |
| 20. | All C.P. Fittings and accessories, Flush Valves, Bottle trap C.P. Waste, Spreaders, Urinal flush pipes. | Continental | Jaguar Gem Parko |
| 21. | Gun Metal Valves (full way check and globe valves), Ball Cock |  | Leader (ISI) |
| 22. | Stoneware pipes and Gully Traps |  | i) Perfect ii) ISI mark |
| 23. | RCC Pipes |  | ISI mark |
| 24. | C.I. double-flanged sluice valves, Non-Return valve. |  | i) Kirloskar ii) IVC |
| 25. | Butterfly Valve |  | AUDCO C & R iii) IVC |
| 26. | Manhole Cover & Frame | Polycrete | Polycrete Enterprises |
| 27. | PVC flooring | In tiles | Krishna Vinyl i) Bhor |
| 28. | Floor Spring |  | Everite Dorma iii) Doorking |
| 29. | Pre-molded tiles |  | Dovetex |
| 30. | Cold twisted bars for reinforcement. | CTD / TMT Bars | SAIL ii) TISCO |
| 31. | Ordinary Portland Cement | 43 Grade | ACC Prism Jaypee iv) Birla Jute |
| 32. | Shuttering oil |  | Fosroc ii) Cico |
| 33. | Bricks |  | Local first quality with crushing strength of 150 Kg / cm2. |
| 34. | Steel Kitchen Sink |  | Nirali Neelkanth iii) AMC |
| 35. | Aluminum fittings |  | Diamond ii) Nulite |
| 36. | Standard rolled steel section for windows |  | ISI mark. |
| 37. | Sensor controlled auto flush |  | Automat ii) Jaquar. |
| 38. | Centrifugally cast (spun) iron S&S pipes & fittings. | Neco Centri | Jayaswals Neco. Ltd. |
| 39. | Polyethylene water storage tanks. |  | Sintex ii) Polycon |
| 40. | Marble aggregates (Best Quality) |  | Nathdwara ii) Rajrgarh |
| 41. | Water proofing material for cement concrete / mortar |  | ACC Cico iii) Fosroc |
| 42. | C.I. pipes : Class L.A. |  | Kesoram ii) Supra |
| 43. | Polysulphite Sealant |  | Fosroc Piddilite iii) Roffa |
| 44. | Bitumen impregnated |  | Shalimar Tar Product. |
| 45. | Resin based adhesive |  | Fevicol ii) Vamicol |
| 46. | Anchor Fasteners |  | Hilti ii) Greaves Cotton |

LIST OF APPROVED MAKES OF MATERIALS FOR ELECTRICAL WORKS

# ITEM									APPROVED   MAKE

1.	Conduit pipe	BEC/M-KAY make/Painteinside and outside (ISI marked) 16 SWG MS conduit.

2.	Conduits accessories & Junction boxes	All made out of 16G MS sheet

3.	Bushes	Rubber/PVC

4.	Wires PVC insulated and PVC sheathed – FRLS/	National/ Finolex (ISI marked)/Incab / Havell

Control Wires

5.	PVC/XLPE insulated cables	CCI/Fort Gloster/Incab/Finolex

6.	Moulded switches and sockets	MK Electric/North-West/Clipsal/Crabtree

7.	Air circuit breakers / MCCB	GE/L&T/Siemens/Clipsal

8.	Fuse Switches & HRC Fuses	GE/L&T/Siemens

9.	Distribution boards MCB type	MDS(Lexic)/Siemens

10.	Loose Wire box for Distribution boards	MDS(Lexic)/ Siemens / GE

11.	Lighting fixtures	Clipsal/Philips/Thorn

12.	Ceiling fans	Crompton/Orient/ Alstom

13.	MCB’s                                                                     MDS(Lexic)/Siemens/GE/Clipsal

14.	Exhaust fans	Alstom

15.	Cable sockets	Alcon (Heavy gauge)

16.	Holder’s brass of sizes	KAY/SSK

17.	Safe trip /RCCB/ELCB	MDS Lexic/Siemens

18.	GI pipe ‘B’ class	TATA/Jindal/GST

19.	Electrical Switchboards/Feeder Pillars 	Milestone Engineering / Tricolite Electrical Industries/ Ess Aar (Kanpur)

20.	Telephone Wires	National/Finolex

21.	Telephone Tag Blocks 	Krone/Pouyet

22.	Telephone outlets	MK Electric / North West/Clipsal

23.	GI raceways	Milestones Engineering/Tricolite/Ees Aar

24.	PVC raceways	Fixopan/Modi

25.	Panel meters	L&T Rishab/GE

26.	Current Transformers	Gilbert Maxwell/Kappa

27.	Selector Switch	L&T /Kaycee/Siemens

28.	Protective Relays	Alstom/L&T

29.	Electronic Energy Meters	Enercon/L&T

30.	Change Over Switch / SFU	L&T / GE

Note:

Samples of all materials, including above-mentioned items, are approved in writing from the Engineer In – charge, before the materials are procured and brought at site for bulk consumption. The contractor does not procure materials until written clearance is accorded by the Engineer-in-charge.

(Santosh Kumar)

Superintending Engineer

Project wise summary of buildings completed during last three years

Project 		:	One additional block in Hall-IV (54 single seats).

Year of construction 	:	2000-2001

Plinth Area		:	1210 sqm.

Financial sanction 	:	Rs. 78.64  lacs

Actual Cost Incurred 	:

| Sub_Head | Cost (in lacs) | Cost per Sqm. (Rs.) |
| --- | --- | --- |
| Civil Electrical Air –conditioning | 44.55 7.55 --- | --- |
| Total | 52.10 | 4306. 00 |

Richer Specification than Govt. Norms :

- Exposed brickwork.

- Superior specifications in toilets.

- Double shutters in windows (glazed & wire net).

- Higher scale of amenities in rooms.

- High quality painting on external & internal walls.

- Site development i/c extension of link corridor.

_______________

Project 		:	One additional block in Hall-I (57 seats).

Year of construction 	:	1999-2000

Plinth Area		:	1293 sqm.

Financial sanction 	:	Rs. 73 lacs

Actual Cost Incurred 	:

| Sub_Head | Cost (in lacs) | Cost per Sqm. (Rs.) |
| --- | --- | --- |
| Civil Electrical Air –conditioning | 52.67 4.04 --- | --- |
| Total | 56.71 | 4386. 00 |

Richer Specification than Govt. Norms :

- Exposed brickwork.

- Superior specifications in toilets.

- Double shutters in windows (glazed & wire net).

- High quality painting on external walls.

Project 		:	2 nos. additional blocks in Girls Hostel (120 seats).

Year of construction 	:	2002-2003

Plinth Area		:	2054 sqm.

Financial sanction 	:	Rs. 130 lacs

Actual Cost Incurred 	:

| Sub_Head | Cost (in lacs) | Cost per Sqm. (Rs.) |
| --- | --- | --- |
| Civil Electrical Air –conditioning | 100.00 16.00 --- | Anticipated “ --- |
| Total | 116.00 | 5648.00 |

Richer Specification than Govt. Norms :

- Permanent external finish (Grit Plaster).

- Kota stone flooring in staircase, common rooms, canteen, toilets, dinning facility.

- Superior specifications in toilet.

- Glazed tile treatment over sloped roofs.

- Press steel frames of doors & windows.

- Double shutters in windows (glazed & wire net).

- RCC rainwater shoots with glazed tile lining.

- Seamless Centrifugal CI Pipes & fittings (used for the first time).

- Expensive architectural design.

- Higher scale of amenities in rooms.

- High quality painting on internal walls.

____________

Project 		:	One additional block in Hall-V ( 54 seats).

Year of construction 	:	2002-2003

Plinth Area		:	1095 sqm.

Financial sanction 	:	Rs. 48.79 lacs

Actual Cost Incurred 	:

| Sub_Head | Cost (in lacs) | Cost per Sqm. (Rs.) |
| --- | --- | --- |
| Civil Electrical Air –conditioning | 54.00 10.00 --- | Anticipated “ --- |
| Total | 64.00 | 5845. 00 |

Richer Specification than Govt. Norms :

- Exposed brickwork.

- Superior specifications in toilets.

- Double shutters in windows (glazed & wire net).

- Higher scale of amenities in rooms.

- High quality painting on external & internal walls.

- Site development i/c extension of link corridor.

- Kota stone in corridors and staircase.

_______________

Project 	:	New RA Hostel

Year of construction 	:	2002-2003

Plinth Area		:	2750 sqm.

Financial sanction 	:	Rs.176 lacs

Actual Cost Incurred 	:

| Sub_Head | Cost (in lacs) | Cost per Sqm. (Rs.) |
| --- | --- | --- |
| Civil Electrical Air –conditioning | 138 28 ---- |  |
| Total | 166.00 | 6036. 00 |

Richer Specification than Govt. Norms :

- Elegant architectural design (the first of its kind in IITK).

- Superior quality flooring.

- Wooden wardrobes (aesthetically well designed and durable).

- Aluminium door & window frames.

- Aluminium windows with double shutters (glazed and wire net).

- Superior specifications in toilets.

- Well-designed kitchen with tiles, cooking platform and storage cabinets.

- Higher scale of amenities in rooms.

- High quality painting on external & internal walls.

- Site development and landscaping.

- Kota stone in balconies & staircase.

________________

Project 		:	Hall of Residence for Boys No. – VII ( 458 seats).

Year of construction 	:	2002-2003

Plinth Area		:	12450 sqm.

Financial sanction 	:	Rs. 876  lacs

Actual Cost Incurred 	:

| Sub_Head | Cost (in lacs) | Cost per Sqm. (Rs.) |
| --- | --- | --- |
| Civil Electrical Air –conditioning | 665.00 110.00 ---- | --- |
| Total | 775.00 | 6225. 00 |

Richer Specification than Govt. Norms :

- Permanent external finish (Grit Plaster with white cement).

- Kota stone flooring in staircase, entrance lobby, link corridors, canteen, foyer, toilets, dinning facility, courtyards of blocks.

- Superior specifications in toilet.

- Press steel frames of doors & windows.

- Double shutters in windows (glazed & wire net).

- RCC rainwater shoots with glazed tile lining.

- Seamless Centrifugal CI Pipes & fittings (used for the first time).

- Expensive architectural design.

- Higher scale of amenities in rooms.

- High quality painting on internal walls.

- Extensive network of underground RCC sewer line, rainwater drains and water supply grid for horticulture.

- Extensive earth filling, landscaping, internal roads, parking lot, fountain etc.

- Aluminium windows in dinning hall & Administrative Block.

- Green marble wall cladding in dinning hall.

_______________

Project 		:	Hall of Residence for Boys No. – VIII ( 489 seats).

Year of construction 	:	2003-2004

Plinth Area		:	12850 sqm.

Financial sanction 	:	Rs. 875 lacs

Actual Cost Incurred 	:

| Sub_Head | Cost (in lacs) | Cost per Sqm. (Rs.) |
| --- | --- | --- |
| Civil Electrical Air –conditioning | 700.00 105.00 ---- |  |
| Total | 805. 00 | 6265. 00 |

Richer Specification than Govt. Norms :

- A combination of exposed brickwork and two layers plaster with grooves.

- Kota stone flooring in staircase, entrance lobby, link corridors, canteen, foyer, toilets, dinning facility.

- Superior specifications in toilet.

- Press steel frames of doors & windows.

- Double shutters in windows (glazed & wire net).

- RCC rainwater shoots with glazed tile lining.

- Seamless Centrifugal CI Pipes & fittings (used for the first time).

- Higher scale of amenities in rooms.

- High quality painting on internal walls.

- Extensive network of underground RCC sewer line, rainwater drains and water supply grid for horticulture.

- Extensive earth filling, landscaping, internal roads, parking lot, fountain etc.

- Aluminium windows in dinning hall & administrative block.

- Green marble wall cladding in dinning hall.

__________________

Project 		:	Girls Hostel (250 seats).

Year of construction 	:	2000-2001

Plinth Area		:	6159 sqm.

Financial sanction 	:	Rs. 412 lacs

Actual Cost Incurred 	:

| Sub_Head | Cost (in lacs) | Cost per Sqm. (Rs.) |
| --- | --- | --- |
| Civil Electrical Air –conditioning | 339.96 52.48 ----- ---- |  |
| Total | 392.44 | 6372. 00 |

Richer Specification than Govt. Norms :

- Permanent external finish (Grit Plaster).

- Kota stone flooring in staircase, common rooms, canteen, toilets, dinning facility.

- Superior specifications in toilet.

- Glazed tile treatment over sloped roofs.

- Press steel frames of doors & windows.

- Double shutters in windows (glazed & wire net).

- RCC rainwater shoots with glazed tile lining.

- Seamless Centrifugal CI Pipes & fittings (used for the first time).

- Expensive architectural design.

- Higher scale of amenities in rooms.

- High quality painting on internal walls.

- Extensive network of underground RCC sewer line, rainwater drains and water supply grid for horticulture.

- Earth filling and extensive landscaping, internal roads, parking lot etc.

_________________

Project 		:	8 nos. Type-A & 4 nos. Type-B residences for Visiting

Faculty.

Year of construction 	:	2002-2003

Plinth Area		:	1380 sqm.

Financial sanction 	:	Rs. 101 lacs

Actual Cost Incurred 	:

| Sub_Head | Cost (in lacs) | Cost per Sqm. (Rs.) |
| --- | --- | --- |
| Civil Electrical Air –conditioning | 83.00 11.00 --- | Anticipated “ --- |
| Total | 94. 00 | 6812. 00 |

Richer Specification than Govt. Norms :

- External cavity wall with exposed tile work (the first of its kind in IITK)

- Provision of energy efficient measures for thermal comfort such as external cavity wall filled with thermocoal insulation, protection of external walls with roof over hangs, pargola, false roof over RCC slab with an insulating air gap, china mosaic over false roof for heat reflection.

- Elegant & expensive architectural design (the first of its kind in IITK).

- Superior quality flooring.

- Antiskid flooring on accessible terraces at first floor.

- Wooden wardrobes (aesthetically well designed and durable).

- Aluminium door & window frames.

- Aluminium windows with double shutters (glazed and wire net).

- Superior specifications in toilets.

- Well designed kitchen with tiles, cooking platform and storage cabinets.

- Higher scale of amenities in rooms.

- High quality painting on external & internal walls.

- Site development and landscaping i/c extension of link corridor.

- Kota stone in balconies & staircase.

_________________

Project 		:	SIDBI Innovation & Incubation Centre.

Year of construction 	:	2002-2003

Plinth Area		:	1153 sqm.

Financial sanction 	:	Rs. 89.64  lacs

Actual Cost Incurred 	:

| Sub_Head | Cost (in lacs) | Cost per Sqm. (Rs.) |
| --- | --- | --- |
| Civil Electrical Air –conditioning | 71.16 9.13 --- |  |
| Total | 80. 29 | 6964. 00 |

Richer Specification than Govt. Norms :

- RCC frame structure.

- Permanent external finish (Grit Plaster).

- Kota stone flooring in seminar room, passage, staircase, electrical room, pantry and balcony.

- Green / white marble in entrance lobby, reception and toilet.

- Superior specifications in toilet.

- Aluminium frames of doors & windows.

- Aluminium windows.

- Laminated / painted flush door shutters.

- False ceiling in reception area.

- RCC rainwater shoots with glazed tile lining.

- Seamless Centrifugal CI Pipes & fittings (used for the first time).

- Expensive architectural design.

- Higher scale of amenities in rooms.

- High quality painting on internal walls.

- Extensive network of underground RCC sewer line, rainwater drains and water supply grid for horticulture.

- Extensive network of underground RCC sewer line, rainwater drains and water supply grid for horticulture.

- Earth filling and extensive landscaping, internal roads, parking lot, barbed wire fencing etc.

________________

Project 		:	Biological Sciences & Bio Engineering Department

Year of construction 	:	2002-2003

Plinth Area		:	5942 sqm.

Financial sanction 	:	Rs. 481 lacs

Actual Cost Incurred 	:

| Sub_Head | Cost (in lacs) | Cost per Sqm. (Rs.) |
| --- | --- | --- |
| Civil Electrical Air –conditioning | 337.00 79.00 45.00 | Anticipated “ “ |
| Total | 461. 00 | 7758. 00 |

Richer Specification than Govt. Norms :

- RCC frame structure with large spans.

- Basement with RCC retaining walls and water proofing with kota stone.

- Energy efficient measures such as over deck insulation, china mosaic heat reflective surface on top of the roof, external cavity walls filled with insulating thermocoal, argon filled double layer sealed glasses in external windows, large central atrium, building integrated photovoltaic cell in combination with heat resistant glasses over central atrium, passive air-conditioning system etc.

- Extensive pipeline systems for fresh / waste, radioactive wastewater, medical gases.

- Extensive recess wiring for networking, telephone and power cables.

- Centrally air-conditioned.

- 3 nos. ducts below beams in each lab. connected to vertical shaft on one end.

- Permanent external finish (combination of Dovetax Tiles & Grit Plaster with white cement).

- Building is equipped with facility of autoclave, cold room and emergency showers etc.

- 10 Passenger lift.

- High quality mirror optics luminaries.

- Fire fighting arrangement

- Kota stone flooring in external staircases, internal corridors, link corridors, 16 nos. labs, central facilities, lecture rooms, seminar room, student lounge, computer labs, toilet, external staircase, open terraces etc.

- Green marble in entrance lobby and central staircase.

- Expensive false ceiling in corridors.

- Gypsum false ceiling in Principal Investigators’ Rooms & special facility rooms.

- Cavity external walls with thermocoal insulation.

- Acoustic treatment in seminar room.

- Superior specifications in toilet.

- Aluminium frames of doors & windows.

- Aluminium windows.

- Laminated flush doors.

- High quality hardware.

- RCC rainwater shoots with glazed tile lining.

- Seamless Centrifugal CI Pipes & fittings (used for the first time).

- Expensive architectural design.

- Extensive recess wiring in conduits for power, network and telephone cables.

- High quality painting on internal walls.

- Extensive external development.

- Polycarbonate dome in staircase.

- Large span modules and extra floor height.

- Extensive interior work with fountain & cascades in the central atrium.

______________

Project 		:	Lecture Hall Complex (Phase-I)

Year of construction 	:	2001-2002

Plinth Area		:	2177 sqm.

Financial sanction 	:	Rs. 287 lacs

Actual Cost Incurred 	:

| Sub_Head | Cost (in lacs) | Cost per Sqm. (Rs.) |
| --- | --- | --- |
| Civil Electrical Air–conditioning | 156.00 28.00 29.00 |  |
| Total | 213. 00 | 9784. 00 |

Richer Specification than Govt. Norms :

- Large span rooms with sloped roofing & RCC frame structure.

- Centrally air-conditioned lecturer rooms.

- Permanent external finish (combination of Dovetax Tiles & Grit Plaster with white cement).

- Kota stone flooring in corridors, staircase, lecture rooms, lobby, stilted areas and green enclosures.

- Gypsum false ceiling in lecture rooms.

- Under deck insulation in top floor.

- Cavity external walls with thermocoal insulation.

- Acoustic treatment in classrooms.

- Superior specifications in toilet.

- Aluminium frames of doors & windows.

- Aluminium windows.

- Laminated flush doors.

- High quality hardware.

- RCC rainwater shoots with glazed tile lining.

- Seamless Centrifugal CI Pipes & fittings (used for the first time).

- Expensive architectural design.

- Extensive recess wiring in conduits for power, network and telephone cables.

- High quality painting on internal walls.

- Extensive earth cutting, filling, retaining wall etc. for creating an elevated hillock, landscaping, internal roads, parking lot etc.

- Large span modules and extra floor height

_____________

Project 		:	Computer Science & Engineering Department Building

Year of construction 	:	2000-2001

Plinth Area		:	3200  sqm.

Financial sanction 	:	Rs. 355 lacs

Actual Cost Incurred 	:

| Sub_Head | Cost (in lacs) | Cost per Sqm. (Rs.) |
| --- | --- | --- |
| Civil Electrical Air –conditioning | 214.00 46.00 77.00 |  |
| Total | 337. 00 | 10531. 00 |

Richer Specification than Govt. Norms :

- Centrally air-conditioned.

- Permanent external finish (combination of Dovetax Tiles & Grit Plaster with white cement).

- 8 Passenger lift.

- High quality mirror optics luminaries.

- Fire fighting arrangement

- Kota stone flooring in corridors, lecture rooms, library, student lounge, computer labs, toilet, external staircase, open terraces etc.

- Granite flooring in entrance foyer and staircase & Head’s room.

- Expensive false ceiling in corridors.

- Gypsum false ceiling in entire building except corridors.

- Under deck insulation in top floor.

- Cavity external walls with thermocoal insulation.

- Acoustic treatment in lecture rooms.

- Superior specifications in toilet.

- Aluminium frames of doors & windows.

- Aluminium windows.

- Laminated flush doors.

- High quality hardware.

- RCC rainwater shoots with glazed tile lining.

- Seamless Centrifugal CI Pipes & fittings (used for the first time).

- Expensive architectural design.

- Extensive recess wiring in conduits for power, network and telephone cables.

- High quality painting on internal walls.

- Extensive external development.

- Elaborate fountain with cascade.

- Polycarbonate dome in staircase.

- Large span modules and extra floor height.

_____________

Project 		:	Samtel R&D Building.

Year of construction 	:	2002-2003

Plinth Area		:	1547 sqm.

Financial sanction 	:	Rs. 195 lacs

Actual Cost Incurred 	:

| Sub_Head | Cost (in lacs) | Cost per Sqm. (Rs.) |
| --- | --- | --- |
| Civil Electrical Air –conditioning | 112.00 30.00 31.00 |  |
| Total | 173. 00 | 11183. 00 |

Richer Specification than Govt. Norms :

- Centrally air-conditioned.

- Permanent external finish (combination of Dovetax Tiles & Grit Plaster with white cement).

- Kota stone flooring in corridors, ramp, seminar room, conference room, lobby, stilted areas and a few labs.

- Green & white marble in entrance foyer, staircase and bands in corridors.

- Granite flooring in meeting rooms and Head’s room.

- Vitrified tile flooring in 2 nos. labs. And PVC flooring in one lab.

- Granite counters in all labs.

- Expensive false ceiling in corridors.

- Gypsum false ceiling in Seminar, conference, student’s dens, computer labs, studio, Head’s room.

- Under deck insulation in top floor.

- Cavity external walls with thermocoal insulation.

- Acoustic treatment in seminar & conference rooms.

- Superior specifications in toilet.

- Aluminium frames of doors & windows.

- Aluminium windows.

- Laminated flush doors.

- High quality hardware.

- Special duct for suction of obnoxious fumes.

- RCC rainwater shoots with glazed tile lining.

- Seamless Centrifugal CI Pipes & fittings (used for the first time).

- Expensive architectural design.

- Extensive recess wiring in conduits for power, network and telephone cables.

- High quality painting on internal walls.

- Extensive earth cutting, filling, retaining wall etc. for creating an elevated hillock, landscaping, internal roads, parking lot, etc.

- Large span modules and extra floor height

_____________